WHMIS

Eyewash

Station

Hearing

Protection

Lens Cleaning

Station

Safety Glasses

Required

s

# Text boxes

## Use Push Stick

Use Hearing Protection

Keep Fingers

5 cm from

Sanding Belt

Keep Fingers

5 cm from

Sanding Disk

Use Hold-Down Guard

Stand to Sides of

### Planer Mouth

Always Clamp

Workpiece

Noise Protection

Required

Maximum

1/16" to 1/8"

Guard Gap

Use Hold-Down Guard

Safety Glasses

Required

Use Clamping Device

## Always Clamp

Workpiece

## Always Clamp

Workpiece

Use Hold-Down Guard

Use Hold-Down Guard

## Always Clamp

Workpiece

## Always Clamp

Workpiece

NAME OF EQUIPMENT:   Floor Jacks

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Use on firm flat floor or ground.

- Always use safety stands to hold up vehicle.

- Ensure that stands are placed on the vehicle frame and are set at the same height.

NAME OF EQUIPMENT:   Air Compressor

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Never point an air nozzle at any part of your body or at anyone.

- Always wear safety glasses when using any tools that require compressed air to operate.

NAME OF EQUIPMENT:   HOIST

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Know how high you can safely raise a vehicle.

- Make sure vehicle is driven onto the hoist squarely.

- Lifting pads must be on the frame.

- Eye goggles must be worn when working below a vehicle.

NAME OF EQUIPMENT:   Safety Stands

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Must be used on a flat ground surface.

- Must be placed on the frame, sub-frame or vehicle suspension.

NAME OF EQUIPMENT:   Varsol Wash Station

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Use with ventilation.

- Use latex gloves to protect hands.

- Wear eye protection.

- Do not use compressed air to dry a part.

NAME OF EQUIPMENT:   Tire (Wheel) Balance Machine

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Remove any loose stones in tread.

- Make sure tire cover safety switch is working.

- Do not lift safety cover until tire has stopped rotating.

- Ensure floor area is dry.

NAME OF EQUIPMENT:   Tire Machine

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Keep floor as dry as possible to avoid slipping.

- Keep hands clear of the rim and tire when reseating the bead.

NAME OF EQUIPMENT:   Photo Chemical

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Avoid skin and mouth contact.

- Wash hands after using chemicals.

- Refer to MSDS binder for further information.

NAME OF EQUIPMENT:   Screen Printing Chemicals

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Avoid skin and mouth contact.

- Wash hands after using chemicals.

- Refer to MSDS binder for further information.

NAME OF EQUIPMENT:   Tape Dispenser

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Use caution when cutting the tape.

NAME OF EQUIPMENT:   Screen Printing Ink

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Avoid skin and mouth contact.

- Wash hands after using chemicals.

- Wash hands after using ink.

- Refer to MSDS binder for further information.

NAME OF EQUIPMENT:   Heat Press

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Do not touch the element and the platen.

##### NAME OF EQUIPMENT:   Blueprint Making Machine

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Do not look directly at the ultraviolet light.

NAME OF EQUIPMENT:   Darkroom – Electric Equipment

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Ensure hands are dry when using any electrical equipment in the darkroom.

NAME OF EQUIPMENT:   Knife, Compass & Scissors

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Handle or carry with sharp end pointing towards the floor.

- Hand or pass sharp objects handle first.

- Avoid touching sharp edges.

NAME OF EQUIPMENT:   Airbrush & Ink

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Avoid skin and mouth contact.

- Do not point the airbrush at anyone.

- Wash hands after using chemicals.

- Refer to MSDS binder for further information.

NAME OF EQUIPMENT:   Paper Cutter

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Keep hands out of cutting path.

- On shear style handle, leave in down position when finished.

NAME OF EQUIPMENT:   UV Exposure Unit

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- If the UV light is visible, do not look at it.

NAME OF EQUIPMENT:   Wash Sink

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Never point the nozzle at anyone.

- If the floor around the washsink becomes wet, it should be mopped immediately.

NAME OF EQUIPMENT:   Stationery Grinder

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Do not wear gloves.

NAME OF EQUIPMENT:   Squaring Shear

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Keep fingers and feet away from moving parts.

NAME OF EQUIPMENT:   Drill Press

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Always clamp material.

- Remove chuck key from chuck.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Make all adjustments with the power off.

- Joint faces and edges only.

- Do not joint wood less than 12” long.

- Use a hold-down push block for jointing surfaces.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

NAME OF EQUIPMENT:   Jointer

NAME OF EQUIPMENT:   Etchant Tank

###### Ferric Chloride/

###### Ammonia Persulphate

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Wear proper safety gear to avoid skin contact (e.g., gloves, apron).

- Refer to “Ferric Chloride” or “Ammonia Persulphate” in MSDS binder for further information.

NAME OF EQUIPMENT:   Wood Lathe

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Check that wood is secure before starting.

- Position the tool rest to within 3 mm (1/8”) of the wood.

- Remove the entire tool rest assembly before sanding.

NAME OF EQUIPMENT:   Router Table

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Use a router bit guard whenever possible.

- Feed the material in the correct direction.

NAME OF EQUIPMENT:   Thickness Planer

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Do not plane wood less than 12” long.

- If wood gets stuck, turn off power then lower the table.

- Check wood for loose knots and foreign materials before planing.

NAME OF EQUIPMENT:   Band saw

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Lower the guard to within 3 mm (1/8”) of the wood.

- Keep hands 5 cm (2”) away from the cut line.

- Cut slowly without forcing the material.

NAME OF EQUIPMENT:   Compound Mitre Saw

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Secure wood against fence.

- Allow the saw blade to reach maximum speed before it contacts the wood.

- Keep hands a safe distance from the blade (15 cm [6”] away).

NAME OF EQUIPMENT:   Radial Arm Saw

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Secure wood against the fence.

- Pull saw forward with a controlled speed.

- Keep hands 12” away from the blade.

NAME OF EQUIPMENT:   Scroll Saw

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Ensure that the pressure foot is resting on the wood.

- Cut slowly, guiding the wood gently with thumbs and fingers.

- Keep hands a safe distance from the blade – never directly in front.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Always use a fence or mitre guide.

- Never stand directly in line with the saw blade.

NAME OF EQUIPMENT:   Table Saw

NAME OF EQUIPMENT:   Spindle Sander

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Feed wood in the direction opposite to the direction that the spindle turns.

- Use the smallest table insert that can surround the spindle.

- Press wood lightly against the spindle.

- Keep wood tight against the table top.

NAME OF EQUIPMENT:   Shaper

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with guards in place.

- Feed wood against the rotation of the cutters.

NAME OF EQUIPMENT:   Combination Belt/Disc Sander

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Hold wood flat against the table top.

- Press wood lightly against the belt/disk.

- Call the teacher if the belt is not tracking straight.

NAME OF EQUIPMENT:   Drill Press

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Tightly secure all materials to the table when drilling.

- Never drill metals without proper clamps.

- Adjust table height and make depth adjustments before power is turned on.

NAME OF EQUIPMENT:   Bench Grinder

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with shield in place.

- Keep the tool rest within 3mm (1/8”) of the grindstone.

- Do not grind against the side of the stone.

NAME OF EQUIPMENT:   Mortising Machine

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Keep a slight gap between the hollow chisel and the bit to avoid overheating.

- Tightly secure wood to the tabletop.

- Make all table and depth adjustments with the power off.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

NAME OF EQUIPMENT:   Horizontal Band Saw

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

NAME OF EQUIPMENT:   Buffing Wheel (felt, wire)

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Operate only with shield in place.

- Apply work only to the lower part of the wheel.

- Do not wear gloves.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

NAME OF EQUIPMENT:   Crucible Furnace/

Enameling Furnace

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn (e.g., face shield).

- Wear proper safety gear (e.g., apron, gloves).

- Remove jewelry, eliminate loose clothing and confine long hair.

- ONLY the instructor pours molten metal.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Only use hand tools for the job they were designed to do.

- Never use cheater bars, handles, or pipes to gain additional leverage.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

NAME OF EQUIPMENT:   Hand Tools

NAME OF EQUIPMENT:   Sand Blaster

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

NAME OF EQUIPMENT:   Arc Welder

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn (e.g., helmet).

- Wear proper safety gear (e.g., gloves, apron).

- Remove jewelry, confine long hair.

- No nylon or loose clothing.

- Make sure area is well ventilated.

NAME OF EQUIPMENT:   Slip Roll

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Do not exceed capacity of machine.

NAME OF EQUIPMENT:   Bar Folder

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Do not exceed capacity of machine.

NAME OF EQUIPMENT:   Squaring Sheer

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Do not exceed capacity of machine.

NAME OF EQUIPMENT:   Box and Pan Brake

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Do not exceed capacity of machine.

- Keep machine in either open or closed position.

NAME OF EQUIPMENT:   Oxygen Acetylene Outfit

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn (e.g., goggles with a # 5 lens).

- Wear proper safety gear (e.g., gloves, apron).

- Remove jewelry, eliminate loose clothing and confine long hair.

- Make sure area is well ventilated.

- Do not exceed 15 psi on acetylene regulator.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn (e.g., face shield).

- Wear proper safety gear (e.g., gloves, apron).

- Remove jewelry, eliminate loose clothing and confine long hair.

NAME OF EQUIPMENT:   Spot Welder

NAME OF EQUIPMENT:   Metal Lathe

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn.

- Remove jewelry, eliminate loose clothing and confine long hair.

- Remove chuck key from chuck.

- Start at low speed.

- Ensure work is securely in the chuck or between centers before starting.

NAME OF EQUIPMENT:   Mig Welder

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Eye protection must be worn (e.g., welding helmet).

- Wear proper safety gear (e.g., gloves, apron).

- Remove jewelry, eliminate loose clothing and confine long hair.

- Make sure area is well ventilated.

NAME OF EQUIPMENT:

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

NAME OF EQUIPMENT:

NAME OF EQUIPMENT:

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

NAME OF EQUIPMENT:

- Operate only with teacher’s permission, and only after operation & safety procedures have been demonstrated.

### FLOORS

- Keep floors free of debris.

- Clean up messes/spills immediately.

- Use “floor-dry”/absorb-all” for oil-based spills.

- Use plenty of water for acid spills.

- Refer to MSDS binder for further information regarding spills/clean ups.

#### HOT METAL AREAS

## CAUTION

# CAUTION